## Slide 1
SMART FIRE
DETECTION SYSTEM
Wi-Fi Connected Fire Alarm with WhatsApp Alerts
ESP32
Wi-Fi
WhatsApp
Technical Presentation • Version 1.0

## Slide 2
Agenda
01
Project Overview
Purpose and objectives
02
Hardware Components
ESP32, sensor & buzzer
03
Software Architecture
Code flow and logic
04
WhatsApp API
CallMeBot integration
05
Setup & Demo
Wiring and deployment
06
Improvements
Future roadmap

## Slide 3
01 Project Overview
What is it?
An IoT-based fire alarm system built on the ESP32 microcontroller. It monitors a digital flame sensor and responds instantly when fire is detected.
Continuous flame sensor monitoring
Local buzzer alarm activation
Real-time WhatsApp notification
Startup readiness confirmation
Serial debug output at 115200 baud
ESP32
Microcontroller
Wi-Fi
Connectivity
WA
WhatsApp Alerts

## Slide 4
02 Hardware Components
ESP32
Dual-core 240MHz
Built-in Wi-Fi & BT
Flame Sensor
Digital IR sensor
DO output on GPIO 32
Active Buzzer
5V compatible
Output on GPIO 33
Wi-Fi 802.11
2.4 GHz b/g/n
HTTPS connectivity
PIN ASSIGNMENT
GPIO 32 | Flame Sensor (INPUT) — HIGH = fire detected
GPIO 33 | Active Buzzer (OUTPUT) — HIGH = alarm ON

## Slide 5
03 Software Architecture
setup()
Init Serial, GPIO, Wi-Fi → send ready message
loop()
Read GPIO 32 every cycle
Fire = 1?
Digital sensor output check
sendAlert()
Build URL → HTTP POST → log response
Libraries Used
WiFi.h
ESP32 Wi-Fi management
HTTPClient.h
HTTPS POST requests
UrlEncode.h
Message URL encoding
Buzzer stays ON while sensor reads HIGH

## Slide 6
04 WhatsApp API Integration
https://api.callmebot.com/whatsapp.php?phone={number}&apikey={key}&text={message}
phone
E.164 format number
e.g. +201019972777
apikey
Personal key from
CallMeBot WhatsApp bot
text
URL-encoded message
via UrlEncode library
HTTP RESPONSE CODES
200
Success — message delivered
401
Unauthorized — invalid API key
429
Rate limit — reduce frequency
To get your API key: open WhatsApp → add +34 644 59 21 83 → send: I allow callmebot to send me messages

## Slide 7
03 Code Walkthrough
void loop() {
bool sensorValue = digitalRead(Sensor);
if (sensorValue == 1) {
digitalWrite(Buzzer, HIGH);
sendAlert("Warning! Fire Detected...");
} else {
digitalWrite(Buzzer, LOW);
}
}
void sendAlert(String message) {
String url = API_BASE + phone + apiKey
+ "&text=" + urlEncode(message);
HTTPClient http;
int code = http.POST(url);
}
Read sensor GPIO 32
WhatsApp alert fired

## Slide 8
05 Setup Guide
1
Install Arduino IDE & ESP32 Board Package
2
Install UrlEncode library via Library Manager
3
Configure Wi-Fi, phone number & API key
4
Upload sketch to ESP32 via USB
5
Open Serial Monitor (115200) & verify output
6
Test: bring flame near sensor

## Slide 9
06 Known Issues & Improvements
Current Limitations
Alert sent on every loop cycle → API rate limit (429)
No Wi-Fi reconnection logic if connection drops
Credentials hardcoded in source file
Single sensor — no multi-zone detection
Suggested Improvements
Add alertSent flag to limit to 1 alert per event
Implement Wi-Fi reconnection in loop()
Store credentials in EEPROM / use provisioning
Add OLED display for local status
Integrate MQTT for IoT dashboard
Quick Fix:
if (sensorValue == 1 && !alertSent) { sendAlert(...); alertSent = true; }

## Slide 10
Thank You
Smart Fire Detection System
ESP32 • Wi-Fi • WhatsApp API • Arduino C++
Questions?